Dense sub-graphs
Introduction to Network Science
Carlos Castillo
Topic 22

---
Sources
- Barabási 2016 Chapter 9
- Networks, Crowds, and Markets Ch 3
- C. Castillo (2017) Dense Sub-Graphs
- Tutorial by A. Beutel, L. Akoglu, C. Faloutsos [Link]
- Frieze, Gionis, Tsourakakis: “Algorithmic techniques for modeling and mining large graphs (AMAzING)” [Tutorial]
- A survey of algorithms for dense sub-graph discovery [link]

---
Density-based methods

---
Density measures
- Density = Average degree =
  - Sometimes just
- Edge ratio =
- What is ?
2 |E| / |V|
|E| / |V|
\frac{2|E|}{|V|(|V|-1)}
|V|(|V|-1)/2

---
Densest sub-graph

---
Goldberg’s algorithm
(exact and deterministic)

---
Goldberg's algorithm (1)
Slides on this section from: http://www.math.cmu.edu/~ctsourak/amazing.html

---
Goldberg's algorithm (2)

---
Goldberg's algorithm (3)

---
Goldberg's algorithm (4)

---
Goldberg's algorithm (5)
If this exists for non-empty S, then S is a sub-graph of density c

---
Example
b
a
c
d
e
Is there S with d(S) ≥ 2?
d(S) = 2 |E(S,S)| / |S|

---
Example (cont.)
2
2
2
3
s
t
2
3
2
1
Is there S with d(S) ≥ 2?
d(S) = 2 |E(S,S)| / |S|
Is there an s-t cut with cost ≤ 10?
 (2|E| = 10)
2
1

---
Example (cont.)
Yes!
2
2
cost = 10
2
3
s
t
2
3
2
1
Is there S with d(S) ≥ 2?
d(S) = 2 |E(S,S)| / |S|
Is there an s-t cut with cost ≤ 10?
 (2|E| = 10)
2
1

---
Example (cont.)
Yes!
2
2
cost = 10
2
3
s
t
2
3
2
1
Is there S with d(S) ≥ 2?
d(S) = 2 |E(S,S)| / |S|
Is there an s-t cut with cost ≤ 10?
 (2|E| = 10)
2
1

---
Goldberg's algorithm (6)
- to find the densest subgraph perform binary search on c
  - logarithmic number of min-cut calls
  - each min-cut call requires O(|V||E|) time
- problem can also be solved with one min-cut call using the parametric max-flow algorithm

---
Charikar’s algorithm
(approximate and randomized)

---
Charikar’s algorithm
- Charikar, M. (2000). Greedy approximation algorithms for finding dense components in a graph. In APPROX.
- Approximate algorithm (by a factor of 2)
  - If the optimal density is λ, in the worst case (if you’re very unlucky!) you will get density λ/2

---
Greedily remove nodes
(break ties randomly)
Compute density as |E|/|V|

---
Exercise
Density =
Draw in Nearpod Draw-it
https://nearpod.com/student/
Code to be given during class
\frac{|E|}{|V|}

---
Example run
Done!

---
Example run
15/11=1.36
14/10=1.40
13/9=1.44
12/8=1.50
11/7=1.57
9/6=1.50
8/5=1.60
6/4=1.50
Density =
3/3=1.00
1/2=0.50
0/1=0.00
\frac{|E|}{|V|}

---
Example run
15/11=1.36
14/10=1.40
13/9=1.44
12/8=1.50
11/7=1.57
9/6=1.50
8/5=1.60
6/4=1.50
Done!
3/3=1.00
1/2=0.50
0/1=0.00

---
Advanced materials
(not included in the exam)

---
Approximation guarantee
- S* = optimal sub-graph (highest density)
- density(S*) = λ = |e(S*)| / |S*|
- For all v in S*, deg(v) >= λ, because
Because of optimality of S*
https://people.cs.umass.edu/~barna/paper/dense-subgraph-full.pdf
\frac{|e(S^*)|}{|S^*|} \ge \frac{|e(S^* \backslash v)|}{|S^* \backslash v|} = \frac{|e(S^*)|-deg_{S^*}(v)}{|S^*|-1}

---
Approximation guarantee (cont)
Hence,
\frac{|e(S^*)|}{|S^*|} \ge \frac{|e(S^* \backslash v)|}{|S^* \backslash v|} = \frac{|e(S^*)|-deg_{S^*}(v)}{|S^*|-1}
deg_{S^*}(v) \ge \frac{|e(S^*)|}{|S^*|} = \operatorname{density}(S^*) = \lambda

---
Approximation guarantee (cont.)
- Now, let's consider when greedy removes the first vertex of the optimal solution
- At that point, all the vertices of the remaining subgraph (S) have degree >= λ, because v has degree >= λ
- Hence, this subgraph has more than edges, and density more than
  Hence this is a 2-approximate algorithm
v \in S^*
\frac{\lambda |S|}{2}
\frac{\frac{\lambda |S|}{2}}{|S|} = \frac{\lambda}{2}

---
Summary

---
Things to remember
- Goldberg’s algorithm
  - How to write the construction for a given graph
- Charikar’s algorithm
  - How to run it on a given graph
- Practice executing these algorithms in small graphs
- If useful for you, write code for these algorithms

---
Practice on your own
Consider the graph on the right, which contains a subgraph with density d(S) = 2|E(S, S)|/|S| equal to 5/2.
Draw the graph of Goldberg’s construction, and in that graph, draw the s − t cut that crosses some of the original edges and proves that a subgraph of density 5/2 exists.
Indicate clearly (1) the cost of each edge in the construction, (2) the desired target cost as a function of |E|, (3) the cost of the cut you found, and (4) the sub-graph the method finds.

---
Practice on your own (cont.)
- Consider the graph on the right.
- Run Charikar’s randomized algorithm for densest subgraph, indicating all intermediate graphs and their density, and marking clearly the graph with the largest density.
- For density use |E|/|V| where |E| is the number of edges in the subgraph and |V| the number of nodes in the subgraph.